## Slide 1
Project Ascension Quad Chart
Project Sketch
Project Description, Opportunity, Objectives
Drone and Ground Robot Communicate to Autonomously Navigate Course
Drones Delivering Packages From Trucks, Drones Monitoring Conditions for Ships
Drone and Groundbot Read QR Codes On Boxes to Determine which Box to go to
Technical Approach
Tello Drone Training Drone
Homemade Drone: STM32F722RET6 FC, SX1280 Transmitter/Receiver, Custom-Made Body, RunCam Phoenix Camera, PX4 Software
Groundbot: PL1 Rover Body, Homemade H-bridge/Buck Converter, Jetson Nano, Python Ground Control Software
Summary Budget and Gantt Chart
Estimate: 31,688.83
Running: 2,936.77

## Slide 2: Project Ascension
Steve Gillet – Software Engineer
Rishikesh – Hardware Engineer
Isaac Mondragon – integration engineer
pew pew
Not

## Slide 3: Project Description
Drone Starts On Groundbot
Drone Takes Off and Hovers First Box and Groundbot Enters First Box
Reads QR Code Inside Box and Drone Goes to Find That Box
Groundbot Enters That Box and Process Repeats

## Slide 4: Software FlowChart
Start Search Pattern
Groundbot Stores Next QR Code
Drone Finds Next QR Code
Drone Stops and Groundbot Goes to Drone
Groundbot Sees Box and Goes Inside
Don’t Do It!

## Slide 5: QRCode Detection Drone-Side
Drone software to detect QR Codes using OpenCV
Concern with Accuracy and Looking Down
Drone Video on Ground Control Software
Getting Video From Drone on Ground Control Software
Python Wifi Sockets and OpenCV and H264 Decoder

## Slide 6
Future Components?
Servo Motor
Distance Sensors
Transceiver
GRound Robot
Components
9.6 Volt Battery (2000 maH)
H-Bridge
Buck Converter (5V-3A)
Jetson Nano
-Linux, supports OpenCV , 40 pin headers, parallel processing
Raspberry Pi Camera (Photo Resolution: 3280 x 2464 pixel : Video Resolution: 1080p30)

## Slide 7: Ground Robot control
Object Detection
Object Tracking
Using OpenCV
Leads the Ground Robot to Box underneath
Finds Entry and Exit Point Using IR Sensors
Process Repeats Till The Last Box
The Robot Transmits
“DONE” Command to the Drone.
The Drone Lands Back on the Ground Robot

## Slide 8: Gantt Chart

## Slide 9: Budget CHart

## Slide 10: Credits
Tello Picture: https://www.igeekphone.com/30-off-dji-tello-mini-drone-hd-5mp-wifi-fpv-for-just-99-99/
Octodrone picture: dronedj.com

## Slide 11: Thank you?
Flora@contoso.com
http://www.contoso.com/